## Slide 1
HUMANOID ROBOT – ASSEMBLING AND PROGRAMMING
…Nurturing STEM Skills for the future
www.brainiacs.com.ng
Learn, Play, Innovate
Coding
Robotics
Games and Apps Development
3D Printing

## Slide 2
Learn, Play, Innovate
Knowledge Harvest
www.brainiacs.com.ng
How do describe a humanoid robot ?
What is 3D modelling and how does it apply to designing a humanoid robot?
How do you convert a 3D model into a format suitable for 3D printing?
Notes: Run a virtual bee-bot

## Slide 3
www.brainiacs.com.ng
Learn, Play, Innovate
Wow Factor

## Slide 4: Key Skills to Learn
Critical Thinking.
Computational Thinking
Team Work.
Analytical Reasoning.
Creativity
www.brainiacs.com.ng
Learn, Play, Innovate

## Slide 5
www.brainiacs.com.ng
Learn, Play, Innovate
At the end of the lesson the pupils should be able to:
Identify materials required to build a humanoid robot.
Assemble a humanoid robot.
iii. Program a humanoid robot to make a simple directional movement as well as sense an obstacle.
Learning Objectives

## Slide 6
www.brainiacs.com.ng
Learn, Play, Innovate
To design a Humanoid Robot the following materials will be needed:
Arduino Nano ii. Arduino Nano Shield iii. USB Cable
iv. Ultrasonic Sensor v. Buzzer vi. Jumper cable
Materials Needed to Assemble a Humanoid Robot

## Slide 7
www.brainiacs.com.ng
Learn, Play, Innovate
To assemble a Humanoid Robot the following materials will be needed:
vii. Micro Servo viii. Switch ix Screws
x. AA Battery Holder xi AA Battery . 3D designs
Materials Needed to Assemble a Humanoid Robot

## Slide 8
www.brainiacs.com.ng
....Learn, Play, Innovate
Assembling a Humanoid Robot
In our previous class, we worked on assembling your 3D designs and we got the design shown below;
Notes: 3D printing also called additive manufacturing is a process of making three dimensional solid objects from a digital file.
3D printed object are created using additive processes.
In an additive process, an object is created by laying down successive layers of material one layer at a time, from the bottom upwards.

## Slide 9
www.brainiacs.com.ng
....Learn, Play, Innovate
Assembling a Humanoid Robot
At this stage, we will establish the necessary connections to ensure our humanoid robot functions properly using the listed materials and following the steps below;
STEP 1: Connect the Battery holder to the switch as shown below;
Notes: 3D printing also called additive manufacturing is a process of making three dimensional solid objects from a digital file.
3D printed object are created using additive processes.
In an additive process, an object is created by laying down successive layers of material one layer at a time, from the bottom upwards.

## Slide 10
www.brainiacs.com.ng
....Learn, Play, Innovate
Assembling a Humanoid Robot
Step 3: Attach the ultrasonic sensor to the head of the robot and connect jumper to the terminals as shown below;
STEP 2 : Attach the Arduino Nano to the Arduino Shield as shown below;
Notes: .

## Slide 11
www.brainiacs.com.ng
....Learn, Play, Innovate
Assembling a Humanoid Robot
STEP 4: On the table below make your servo connections as directed;
Servo | Signal Pin (Yellow) | 5V (Red) | Ground (Brown)
Right Arm Servo | Pin 10 | V | G
Left Arm Servo | Pin 11 | V | G
Right Hip Servo | Pin 3 | V | G
Left Hip Servo | Pin 6 | V | G
Right Feet Servo | Pin 5 | V | G
Left Feet Servo | Pin 9 | V | G
Notes: .

## Slide 12
www.brainiacs.com.ng
....Learn, Play, Innovate
Assembling a Humanoid Robot
STEP 5: As directed on the table below, connect your ultrasonic sensor as seen;
Ultrasonic Sensor | Pins
Vcc | V
Trig | Pin 8
Echo | Pin 7
Gnd | G
STEP 6: As shown below, connect your buzzer as instructed;
Buzzer | Pins
Positive Pin (Long Pin) | Pin 2
Negative Pin (Short Pin) | G
Notes: .

## Slide 13
www.brainiacs.com.ng
....Learn, Play, Innovate
Assembling a Humanoid Robot
STEP 6 : Connect your AA battery holder to the Circuit as shown on the table and picture below;
AA Battery Holder | Pin
Positive Terminal (+ve) | Vin
Negative Terminal (-ve) | Gnd
Notes: .

## Slide 14
www.brainiacs.com.ng
....Learn, Play, Innovate
Assembling a Humanoid Robot
STEP 7 : Cover your robot and Attach your battery holder to your robot with help of a glue gun and you should have this;
Notes: .

## Slide 15
www.brainiacs.com.ng
....Learn, Play, Innovate
Programming a Humanoid Robot
At this moment, we have successfully completed the assembly and making of all necessary connections our robot. Now, we are ready to proceed with programming.
Next, click on the following link to download and install the https://support.arduino.cc/hc/en-us/articles/360019833020-Download-and-install-Arduino-IDE to download and install ARDUINO IDE.
STEP 1: Click here to download and install your ARDUINO IDE
Notes: .

## Slide 16
www.brainiacs.com.ng
....Learn, Play, Innovate
Programming a Humanoid Robot
STEP 2: After installing your ARDUINO IDE software, launch it and you should have this environment below;
STEP 3: Click on this link https://drive.google.com/file/d/1EIKH9bHLRdULcg2vNqZWIz1DZRE3ke_B/view?usp=drive_link to download your humanoid robot code.
Notes: .

## Slide 17
www.brainiacs.com.ng
....Learn, Play, Innovate
Programming a Humanoid Robot
Step 4: Click here to select the microcontroller board and port
Notes: .

## Slide 18
www.brainiacs.com.ng
....Learn, Play, Innovate
Programming a Humanoid Robot
Step 5: Scroll down to search for Arduino Nano and click on it
Step 6: Click on ‘OK’
Notes: .

## Slide 19
www.brainiacs.com.ng
....Learn, Play, Innovate
Programming a Humanoid Robot
Step 7: Click on ‘TOOLS’ and scroll down to select PROCESSOR
Step 8: Select ATmega328P(Old Bootloader) and click on it.
Notes: .

## Slide 20
www.brainiacs.com.ng
....Learn, Play, Innovate
Programming a Humanoid Robot
Step 9: Click here to verify the code
Step 10: Immediately you are done verifying your code, click here to upload your code into your Arduino Nano to allow robot work.
Notes: .

## Slide 21
www.brainiacs.com.ng
....Learn, Play, Innovate
Recap
At the end of the lesson, pupils were able to:
Identify materials required to build a humanoid robot.
Assemble a humanoid robot.
Program a humanoid robot to make a simple directional movement as well as sense an obstacle.

## Slide 22
Thank you!
www.brainiacs.com.ng
Learn, Play, Innovate

## Slide 23: How you can get to us
Twitter: Brainiacs_Ng
Phone No: +234 909 109 5057
Email: brainiacsng@gmail.com
      info@brainiacs.com.ng
Website: www.brainiacs.com.ng
google+: brainiacsng
Youtube Channel: Brainiacs_Ng
www.brainiacs.com.ng
Learn, Play, Innovate